## Slide 1: System/Subsystem Design Description for ArcLight Automation Map Bundle Testing
Prepared By: Michael Wolff
August 31, 2015
Revision: 07

## Slide 2: Revision History
Date | Version | Summary
3/25/2015 | 01 | Initial Check-in
3/31/2015 | 02 | Updates based on Desk Review with Shaudi Kheradmand
4/2/2015 | 03 | Minor updates prior to distribution for review
4/15/2015 | 04 | Added Design Review Minutes (at end) and incorporated updates from review
6/2/2015 | 05 | Updates based on SDD, project planning, minor as-built updates
6/22/2015 | 06 | Latest updates for development environment
8/31/2015 | 07 | Final updates for Map Bundle as-built

## Slide 3: Contents (as per ViaSat SSDD template)
1-Scope
  1.1-Identification
  1.2-System Overview
  1.3-Document Overview
2-Referenced Documents
3-System-Wide Design Decisions
4-System Architectural Design
  System Design Overview
  4.1-System Components
  4.2-Concept of Execution
  4.3-Interface Design
    4.3.1-Interface Identification and Diagrams
    4.3.2-Project-Unique Identifier of Interface
5-Requirements Traceability
6-Notes
  6.1-Acronyms
  6.2.-Development Environment
Additional Slides (at end)
  Source Diagrams
  Design Review Minutes
  Action Items

## Slide 4: 1-Scope
1.1-Identification
  This document applies to the ArcLight Automation software for the AL1/AL2 Acceptance Test system in Germantown
    The Phase 1 effort, hence the initial scope of this document, applies to a dedicated ArcLight Map Bundles automated testing subsystem
1.2-System Overview
  See details below
1.3-Document Overview
  This document contains the necessary information to proceed with
    The Software Detailed Design (SDD) for ArcLight Automation of Map Bundle Testing
    The dedicated Map Bundles subsystem development environment.
      Lab/Equipment layout
      Perforce

## Slide 5: 1.2-System Overview
Test Automation Subsystem controls Test Equipment and Unit Under Test
Provides integrated automated testing to produce repeatable regression testing for Map Bundles.
  Trickle Download of Map Bundles Verification
  Map Bundle Upload via Terminal Webpage Verification
  Precedence Verification of Map Bundles
  Forward Link Lock Verification of Map Bundles
Supports simple “LAMP” (Linux, Apache, MySQL, PHP/Python) web-stack for external Browser based test launch management (very basic) interface
Provides Test Results for test suite
System will be developed at the ViaSat Germantown facility
Test Automation
Subsystem
Test Equipment
Unit Under Test (UUT)
Browser

## Slide 6: System Overview-UUT Test Interfaces
Black-box/White-box testing through Interfaces
GUI (HTTP)
  NMS
    NMS Configuration Screens
      including Map File upload (via Trickle)
    EMS Configuration Screens
      Forward Link
        Frequency, Chip Rate
    Status Screens
  Terminal
    Configuration Screens
      including Map File upload
    Status Screens
      Forward Link Lock
CLI CMD (Serial)
  Control of Terminal
  syslog inspection
  Precedence verification
  Validation of map files
Linux (SSH)
  Validation
    scp of files
  CLI via SSH
    Same functionality as CLI CMD)
SQL Query (SSH) – Future, N/A
  Database
    sqlplus
      Scripts for Validation of data
GUI
(HTTP)
SQL Query
(SSH)
CLI CMD
(Serial)
Linux
(SSH)
Unit Under Test (UUT)
DB
NMS
Term

## Slide 7: Deployment Configuration
S4 Catalyst
NetInstall-open SuSE
192.168.136.41
(u:root/p:viasat)
Map Test Appliance – Supermicro Blade #2
EMS (SuSE) Virtual M-2
192.168.136.82
192.168.136.92 192.168.142.5 (VLAN-142)
192.168.136.142 192.168.142.8 (VLAN-142)
192.168.142.18 (VLAN-142)
(u:arclight | u:root / p:Viasat123 | p:viasat | p:Coolsys1)
<testerA>-wxp
<testerB>-wxp
Perforce, Share-point, …
Corp
LAN
Auto(RedHat) Virtual M-5
IPE (SuSeE Virtual M-4
RtNMS(SuSE) Virtual M-3
NMS (SuSe) Virtual M-1
Configuration Notes:
/etc/sysconfig/network
./routes: route add default gw 192.168.142.1 eth0
./ifcfg-eth0
/etc/udev/rules.d/70-persistent-net.rules: (force eth0)
S4 – Trunk Port (V2, V142, V8xx)
PBR – Tag Subnet 142.x as VLAN 142
EFLM
VMBR1520
IF-SMA-RG6
EFLM-Tx
VMBR-Rx
192.168.142.58
(VLAN-142)
(u:root/p:1204_@vsat)
(VLAN-803-81x)
Console Server
SER-1
192.168.136.13
(port: terminal_1-N)
SIG GEN
VSwitch
<testerC>-wxp
Lab Switch/PBR
192.168.136.6-#2 (E2442)
136.6-#8 (E2448)

## Slide 8: Deployment Configuration
Corporate Access for services, i.e. Perforce, Remote Desktop for developers
Blade Server Hardware
  Uses Virtual OS (VMware ESXi) with Virtual Machines (VM)
    NMS, EMS, RtNMS, IPE, Linux VM (for test automation controller); (SuSE/Redhat)
  Ethernet
    ETH1-Lab Switch
      Internal virtual networks to each VM
    ETH2-Terminal
      2nd Port on PowerEdge to VMBR sub-net
        Internal virtual network to:
          Term Win-PC w/ETH2
          Test Linux VM w/ETH2
Terminal Sever
  Access to VMBR (remote terminal) CLI
EFLM
  EHC with EFLM software
EFLM Tx-RF to Signal Generator with SMA connection
  Signal Generator will shift the FL frequency from EFLM
Signal Generator to VMBR Rx-RF L-Band with SMA connection
SW Tools
  Linux VM Tools
    Test VM
      Selenium
      Python
      PHP (TBR)
      Apache
      MySQL
      P4V
      Chrome/FF Browser
  Windows 7
    Chrome/FF Browser
  tool-wxp
    VMware vSphere Client
Alternative Configurations
  VMBR might be accessible from Lab Switch by VLAN if common resource switched between testbeds.
  Use PowerEdge COM1 serial port to connect directly to VMBR serial and eliminate console server
  Connect ETH-2 to Lab Switch if VMBR are shared resources
  Java, Java Script
  Firewall/Router

## Slide 9: 2-Referenced Documents
ID | Name/Description | Location (Perforce, URL, etc.)
REFD010 | AL1_Mapbundles_TestProcedure | //Arclight/ArcLight/AcceptanceTest/Test_Procedures/AL1_Mapbundles_TestProcedure.docx
REFD020 | Automation Plan (as of September 2014) | //Arclight/ArcLight/AcceptanceTest/Automation/Presentation/AL_Automation_Plan.pptx
REFD030 | Selenium Primer | //Arclight/ArcLight/AcceptanceTest/Automation/Presentation/Selenium_Training_Slides.pptx
REFD031 | Selenium Examples | //Arclight/ArcLight/AcceptanceTest/Automation/NMS/
REFD032 | Leapfrog Selenium Example | //Broadband/TestTools/web_performance_automation/selserverstarterhub.py
REFD040 | Existing ArcLight Generic Test Automation Facility (GTAF) scripts | //Arclight/ArcLight/AcceptanceTest/Automation/GTAF_TIDE/
REFD041 | GTAF Wiki Info | https://wiki.viasat.com/pages/viewpage.action?pageId=26443937
REFD050 | Map bundle Precedence example | //Arclight/ArcLight/AcceptanceTest/Automation/Scripts/Maps/find_coords/find_all_coords.m
REFD051 | Map bundle FL Lock example | //Arclight/ArcLight/AcceptanceTest/Automation/Scripts/Maps/maps_bundle.py
REFD060 | Results Database (Reda) | https://wiki.viasat.com/display/Proj/Reda
REFD061 | Reda Examples | //Broadband/TestTools/Reda/
REFD070 | Surfbeam Automation Manager (SAM) | https://wiki.viasat.com/display/Proj/SAM
REFD071 | SAM Examples | //Broadband/TestTools/SAM/

## Slide 10: 3-System-Wide Design Decisions
Use Selenium to control Browser based GUIs
  Selenium IDE for Firefox Browser available for record and play
    Can be exported into Python*, PHP, Java
Linux browser can control Terminal (VMBR)
  Use Chrome per NMS/EMS/Terminal compatability
Provide subsystem integration level testing of Map Bundles; not necessary to explicitly re-verify each test point functionality, e.g.
  FL Lock proves EFLM/VMBR tuning.
  Data persistence validates database, so no sqlplus for this phase.
Coalesce test results for easy inspection of outcome
  MySQL
  Files
    Selenium screen captures
  Status, including file upload, through Browser Interface (TBR)
Parameterization
  Runtime
  Paths

## Slide 11: 4-System Architectural Design
System Design Overview
  HWCIs
    As per Deployed Configuration
  CSCIs
    Existing ArcLight software for all UUT components
    Test VM (Linux) for NMS and Terminal GUI control via Browser
      Terminal (VMBR) on separate subnet
    Python scripts to access Selenium library; see REFD030 – Selenium Examples
      May substitute or augment with PHP
    Apache (LAMP web-stack) to support browser based Automation GUI (very basic) for launching test suite and viewing results.
    MySQL for test results and configuration
    Control Test Equipment
      Signal Generator for Forward Link Lock

## Slide 12: 4.1-System Components
Software Components Overview (CSCI)
  ArcLight Test GUI
    Manages simple set of html webpages for launching tests and getting results
  ArcLight Test Cases
    ArcLight Automation Manager
      Launch script(s) from AL Test GUI or Linux shell
      Common configuration of test database and files
    Utilize API layers to manage devices during execution of test procedures
    Launched from Linux
    Extensible for additional test cases
    Follow standardized results logging
      API (or Reda)
    mapBun Trickle
    mapBun Terminal Upload
    mapBun Precedence
    mapBun FL Lock
  ArcLight GUI, Devices and Database APIs
    Abstractions for project specific customizations
  Common/Generic API layers for abstracting Selenium, Devices, and MySQL
    Leverage test equipment support (GTAF)
    Add support for additional test devices
  Does not preclude the use of GTAF and/or Reda, rather provides for re-use or snap-in replacement.

## Slide 13: 4.2-Concept of Execution
ArcLight Test GUI
  Main Menu
    http://altest.allab.viasat.com/index.html
    Hyperlinks to other screens
  Initiate Test
    Checkbox list
      mapBun Trickle
      mapBun Terminal Upload
      mapBun Precedence
      mapBun FL Lock
    Start Button
  Test Configuration (TBR)
    Set test parameters
    Upload test files
  Test Status w/Results
ArcLight Automation Manager
  Common/Single entry point for launching test script(s)
  Initializes database for test
  Initializes test directories/files
    e.g., KML result files placed here
AL GUI API
  Common ArcLight GUI Routines
    Make selenium calls underneath
    Example: setGuiObjVal(gui {nms|ems}, screen {bundle | etc…}, obj {filename | etc…}, value {string})
ViaSat Selenium API
  Example:
    clickHere(buttonID)
    enterText(inputId)
    enterNumber(inputId)
AL Devices API
  Common ArcLight Device Abstractions
    AL Terminal CLI
Devices API
  Abstracts non-ArcLight devices, e.g. Console Server, Ixia, Linux, ssh
AL Database API
  Common ArcLight Database Abstractions
    Results Records
    Configuration Records
Results API
  Generic Automation Testing API
  May have Apache connector for Results query

## Slide 14: Concept of Execution
mapBun Trickle
NMS
  Copy bundle
  trickle to download the bundles
    Both signed and unsigned
Verification
  successful file transfer to Terminal
mapBun Terminal Upload
Terminal GUI
  Load maps through GUI
CLI
  Get md5 checksum
Verification
  md5 checksum matches for both signed and unsigned

## Slide 15: Concept of Execution
mapBun Precedence
Test Controller
  Generate kml file
  Find all coordinates
    Update existing Matlab scripts, uses inpolygon
      //Arclight/ArcLight/AcceptanceTest/Automation/Scripts/Maps/find_coords/
    Use single, unique coordinate for overlapping regions
      In diagram below, Lat/Long “P2” verifies satellite beam S1 and S2
  Store in db/file; use environment variable
Verification
  Visually inspect KML File
mapBun FL Lock
NMS
  Set FL frequency based on map coordinates
    EMS Configuration
      Set Frequency, Chip Rate
  Compute FL frequency
    Formula:
Terminal
  Load SED/SSCF file bundles
    Optimize if loaded from previous portion of test
  Change the lat/long coordinates of the terminal and turn sat search on.
  Clear syslogMsgs file
  Reboot the system
  grep the syslogMsgs file
  Save satellites locked onto
    Verify the TWP show lock
    Parse the tempLog file (console outputs) printed to the syslogMsgs file
  Terminal reads in coordinates file
Verification
  Examine satellite locking order for correctness

## Slide 16: 4.3-Interface Design
4.3.1-Interface Identification and Diagrams
TBR
4.3.2-Project-Unique Identifier of Interface
Coordinates File Format
  CSV
    Latitude, Longitude Pairs
    One pair per line
Map Files
  sed
  sscf
Runtime Parameters
  Format
    TLV, possibly XML
  Variables
    Bundle File
    Coordinate File
    AL NMS/EMS GUI URL
    Terminal IP
    Password(s)

## Slide 17: 5-Requirements Traceability
Id | Description | Section
1.0.0 | Create Isolated Testbed for Map Bundles Testing | 1.2 Deployed Configuration
1.1.0 | Install all hardware in stand-alone setup | 1.2 Deployed Configuration
1.1.1 | Install One Server with ESXi and the following VMs: NMS, EMS, RtNMS, IPE, Windows 7 VM (for PC co-located to Terminal), Linux (Ubuntu) VM (for test automation controller) | 1.2 Deployed Configuration
1.1.2 | Install EFLM | 1.2 Deployed Configuration
1.1.3 | Install VMBR1520 Modem | 1.2 Deployed Configuration
1.1.4 | Install ASA | 1.2 Deployed Configuration
1.2.0 | Install all ArcLight Software | 1.2 Deployed Configuration
1.3.0 | Verify Terminal(s) can achieve satellite lock | 1.2 Deployed Configuration
2.0.0 | Create Automated Tests for Map Bundles Testing | 4.1 System Components
2.1.0 | Create Trickle Download Test | 4.1 System Components
2.2.0 | Create Terminal Download Test | 4.1 System Components
2.3.0 | Update scripts Find unique coordinates in overlap regions | 4.2 Concept of Execution
2.3.1 | Find points within a contour is the function inpolygon | 4.2 Concept of Execution

## Slide 18: Requirements Traceability
Id | Description | Section
2.3.2 | Clean up all of these scripts so that it flows better. | SDD
2.3.3 | Input of this script should be the name of satellites of interest to find unique coordinates. | SDD
2.3.4 | Output should be a .txt file that has the unique coordinates. | SDD
2.3.5 | The goal is to have a single unique coordinate for overlapping regions | 4.2 Concept of Execution
2.4.0 | Terminal Precedence | 4.1 System Components
2.4.1 | Shall account for any type of password, i.e. password for any terminal build. | 4.3.2-Project-Unique Identifier of Interface
2.4.2 | Make script generic so that any terminal password will be automatically chosen as appropriate to run the script | 4.3.2-Project-Unique Identifier of Interface
2.5.0 | Forward Link Lock | 4.1 System Components
2.5.1 | Automate the NMS GUI so that the FL parameters can be entered via selenium | 4.2 Concept of Execution
3.0.0 | General Automation Requirements | 
3.0.1 | Parameters should be able to be read from a database file (i.e. a csv file) and FL parameters configured accordingly on the NMS GUI. | 4.2 Concept of Execution
3.0.2 | Should be able to poll terminal webpage with selenium to see if terminal has achieved Sat Lock. Once SAT Lock achieved, move onto performing FL lock test for next satellite | 4 System Architectural Design

## Slide 19: Requirements Traceability
Id | Description | Section
3.0.3 | Centralize results for post-processing | 4.1 System Components

## Slide 20: 6-Notes
6.1-Acronyms
Development Environment
  Perforce
  Action Items
Deployment Notes
Open Issues
Other Notes

## Slide 21: 6.1-Acronyms
Acronym | Definition | Comments
ECS | Enhanced Channel Simulator | Used to simulate satellite delay
EFLM | Enhanced Forward Link Modulator | Used for VCSM Forward Link
EHC | Enhanced Hub Canceller | Enhanced Hub Canceller used for PCMA
IPE | IP Encapsulator | Used to encapsulate IP packets
RTNMS | Real-Time Network Management Server | Used to control and manage remote terminals
VMBR | ViaSat Mobile Broadband Router | Remote Terminal used in ArcLight Hub
GTAF | Generic Test Automation Facility | In-house libraries for controlling test devices, i.e. IXIA
CSCIs | Computer Software Configuration Items | 
HWCIs | Hardware Configuration Items | 

## Slide 22: Development Environment – Perforce
Perforce // Arclight /ArcLight /AcceptanceTest /Automation/…)
MapTesting
Maps
find_coords
GTAF_TIDE
Script
utils
TerminalSerialCom.py
src
alam
aldev
altg
apache
mysql
alg
aldb
docs
Scripts
misc
vsel
mapbun
SSDD
SDD

## Slide 23: Development Environment Action Item Details
Acquisition of Lab Items
  PowerEdge
  VMBR
  EFLM
  Signal Generator
  Cables
    SMA
    Ethernet TP
  Power Strips
  Lab Location
  Mounting Rack
  Firewall
  Router

## Slide 24: Deployment Notes
/
MySQL
Apache
/home/altest
Python
Selenium
Define file organization of installed software
  TBR

## Slide 25: Issues
OPEN
None
CLOSED
  For NMS/EMS GUI, rely on screenshot PNG files from scripts since test is not interactive with human
Test Cases
  FL Lock (Closed – added Signal Generator)

## Slide 26: Source Diagram Slides

## Slide 27: System Design Overview
Test Automation Subsystem
Test Equipment
Unit Under Test (UUT)
DB
NMS
VMBR
(Terminal)
RTNMS
EMS
IPE
EFLM
IXIA
ECS
AdTech
Noise Gen
Spec An
VVAU
Signal Gen
Test VM Linux
Apache
Selenium
Browser
Tcl/Expect
Python/PHP
MatLab
Config,
Results, MySQL
https
Console (Serial or SSH)
shell

## Slide 28: Software Components Overview
Test VM Linux
ViaSat Selenium API
AL Test GUI
AL GUI API
Selenium Web Driver
Apache
MySQL
Browser
mapBun
FL Lock
COTS
CSCI
mapBun Term Upload
mapBun Precedence
mapBun Trickle
AL DB API
AL Auto Mgr
Linux libs
Results API
(Reda)
AL Devices API
AL Test Cases
commonCSCI
Devices API
(GTAF)
KEY:
Files
Python
Matlab
shell

## Slide 29: Software Components Overview (v2)
Test VM Linux
ViaSat Selenium API
AL Test GUI
AL GUI API
Selenium Web Driver
Apache
MySQL
Browser
NLG
COTS
CSCI
mapBun
AL DB API
AL Auto Mgr
Linux libs
Results API
(Reda)
AL Devices API
AL Test Cases
commonCSCI
Devices API
(GTAF)
KEY:
Files
Python
Matlab
shell

## Slide 30: Miscellaneous Diagrams
S1:
P1
S2:
P2 P3
= {P2}

## Slide 31: Use Case

## Slide 32: Design Review Minutes
Date: 4/8/2015, 4-5pm EDT
Attendees: Shaudi Kheradmand, Dan Alger, Bryan Workman, Bobby Chiu, Leyla Mosavati, Bryant Schussler, Tom Zhang, Michael Wolff
Location: CR – Germantown - 121 B2 with WebEx and VTC
Subject: Review of //Arclight/ArcLight/AcceptanceTest/Automation/MapTesting/AL_Automation_SSDD.pptx
NOTES:
NMS/EMS GUI Testing
  Must use Chrome
  http only; https is future
  rely on screenshot files from scripts as results artifacts since test is not interactive with human
Forward Link Lock Test
  ECS not necessary for closed loop
  Corner case requires a signal generator since the terminal frequency may be out of the EFLM transmit frequency range.
Must support additional Map bundles formats, specifically GDRM and RLC when present.
Verify that signed and unsigned match checksum
Provide contour verification
If too many points, then intervene with manual points
For NMS/EMS GUI, Reda has many scripts that are PHP (and TCL based), so may use/adapt those wherever possible.
  Some direct API calls to Reda
PHP may make integration with Apache and MySQL easier/faster, so may use that instead.
Action Items:
  (Wolff) Proceed to detailed design. Have informal interim review of high-level portion of SDD in about 2-3 weeks.
  (Shaudi) Acquire Lab equipment specified on SLIDE - Development Environment Action Item Details

## Slide 33: Project Planning
See SDD Review Slides