## Slide 1: Users Manual for ArcLight Automation Appliance
Prepared By: Michael Wolff
February 29, 2016
Revision: 05

## Slide 2: Revision History
Date | Version | Summary
12/14/2015 | 01 | Initial Check-in
12/15/2015 | 02 | Added Info on NLG/Collection
01/12/2016 | 03 | Added more details about NLG/Collection Data Analysis
01/18/2016 | 04 | Added Syslog details about NLG/Collection Data
02/29/2016 | 05 | Added ReDa and Test Utilities details

## Slide 3: Contents
Scope
System Overview
Theory Of Operation
Deployment Configuration
Command and Control
  Home Page
  Test Launch
  Configuration
  Results
    Data Generation
    Status
    Database Export
  Utilities
  ReDa
Use Cases
  Maps
    Process
    Training
  Data Collection
  VMT Commands
Map Testing Process
Map Bundle Training Exercise
NLG Data Analysis
Syslog File Formats

## Slide 4: Scope
This Users Manual addresses the operation of the ArcLight Automation Appliance for Map Bundles and AL1 Acceptance Test testing in Germantown
  Core capabilities
    Phase 1 - dedicated ArcLight Map Bundles automated testing subsystem
    Phase 2 – VMT Data Collection from GUI
    Phase N – Tools to aid in testing
Detailed training for Map Bundle Testing

## Slide 5: System Overview
Describes how the AL Test Automation Appliance works from the Users perspective

## Slide 6: System Overview
Test Automation Subsystem controls Test Equipment and Unit Under Test
Provides integrated automated testing to produce repeatable regression testing for Core Functional Areas
  Map Bundles
      Based on Test Procedure: //Arclight/ArcLight/AcceptanceTest/Test_Procedures/AL1_Mapbundles_TestProcedure.docx
    Map Bundle Upload via Terminal Webpage Verification
    Trickle Download of Map Bundles Verification
    Precedence Verification of Map Bundles
    Forward Link Lock Verification of Map Bundles
  VMT Data collection
Provides Test Results for test suite
  Accessible through AL automation and ReDa webpages
*GROUP
  Each configuration is organized into a “group” which defines the specific NMS, Terminal and Map for those tests

## Slide 7: Theory of Operation
Describes how the AL Test Automation Appliance works internally to control the Unit Under Test

## Slide 8: Theory of Operation
Unit Under Test (UUT)
    Controlled by Automaton Appliance
  NMS/EMS GUI
    NMS Configuration/Status Screens
      File upload (Trickle)
      MAPS
        NMSPM VMT
      VMT Fleet
        Commands (ReLogin)
    EMS Configuration Screens
      Forward Link
      Frequency, Chip Rate
      Hub Tx Enable/Disable
  Terminal GUI
    Configuration Screens
      Map File upload
      Configuration upload
        Baseline for Trickle
    Status Screens
      General, FL, RL, ACU
  Terminal CLI/Shell
    termcmd
      Control of Terminal
        Antenna
        Lat/Long
    syslog
      Precedence verification
      Upload via scp
Automation Browser
    User Interface to control automated tests and review results
    Supports simple “LAMP” (Linux, Apache, MySQL, PHP/Python) web-stack for external Browser based test management interface
    Uses Selenium and Chromedriver to automate GUI operations
  Configuration
    Includes tuning parameters
  Test Launcher (Controller)
  Results
  Utilities
    Map Bundle Test Report
  ReDa
    ViaSat “Standard” Status and Results web interface

## Slide 9: Theory of Operation Additional Designs

## Slide 10: Deployment Configuration
Dedicated NMS/Hub for Map Testing
Access to “any” AL1 NMS and “all” Terminals for Data Collection and VMT Commands

## Slide 11: Deployment Configuration
Corporate Access for services, i.e. Perforce, Web access to Automation for testers
Blade Server Hardware
  Uses Virtual OS (VMware ESXi) with Virtual Machines (VM)
    NMS, EMS, RtNMS, IPE, Linux VM (for test automation controller); (SuSE/CentOS)
  Ethernet
    virtual networks to each VM
EFLM
  EHC with EFLM software
Forward Links
  Normal
    EFLM to Terminal
  Spectral Inversion
    EFLM To Mixer (R)
    Signal Generator to Mixer (L)
    Mixer to Terminal (I)
  Special Pilots
    SAM4/FLM4 to Terminal
    Setup single frequency @SAM and let Automation Tool run test to set Terminal and capture results
Data Collection
  Automation Appliance has IP Connectivity to all Terminals (VLANs 8XX) and all NMS/EMS in 136 subnet

## Slide 12: Command and Control Homepage
Homepage
  http://192.168.136.92/index.html
  Hyperlinks to
    Test Procedures Launch
    Test Results
    Test Configuration
    Test Utilities
    ReDa

## Slide 13: Command and Control Test Launcher
Test Launcher
  Choose Configuration Group(s)
    Examples: “400-410, 413, 500”, or “505”
    Allows for Map serial batch or NLG parallel monitoring
  Check one or more desired tests (user should make good choices)
    Map Bundle
      Terminal Upload
      Trickle
      Precedence
      FL Lock
    NLG
      Poll Start
        Collect NMSPM VMT and Terminal Screen Status
      Poll Term-only Start
        Collect Terminal Screen Status
      Poll Stop
      VMT [Logout/ReLogin/Reboot]
  Click Start Button
  Click “Test Results” to view progress and results

## Slide 14: Command and Control Configuration
Set Group Id
  Use next new, or
  To Edit, set to known id and click load
Set and Save Map Bundle
  Choose file from Perforce Local workspace
  Choose Beam to Test as specified in SSCF (not SED)
  Specify Bundle Version
Set and Save NMS
  Choose 192.168.136.142 for Maps
  Choose any other NMS in 136 subnet for Data Collection
Set and Save Terminal
  Terminal Name must match name in NMS VMT Fleet
  Password must be for the loaded terminal SW version
Set and Save Hub Associate
  Select both Hub1 and Hub2 pulldowns
  For collection, RTNMS syslog will be copied from each hub
  For Map Bundle, Hub1 for EFLM control

## Slide 15: Command and Control Tuning Parameters
Customize algorithm for the group
Precedence Dwell to reduce the SSCF dwell time for satellite search
Hub name (to be deprecated and replaced with the RTNMS Hub Name
FL Rx Freq overrides the frequency from SED; stopgap when SED frequency != 1st entry

## Slide 16: Command and Control Summary Test Results
Summary of each test group
For Map, shows terminal, NMS, Beam
For Collection, shows terminal, NMS
click on Group Id for details

## Slide 17: Command and Control Detailed Group Results
Map Bundle Config Files
  Release Zip
  Bundle Zip
  MD5/Signed SED, SSCF, RLC, GDRM
  MD5 stripped SED, SSCF, RLC, GDRM
Precedence Config
  KLM for Google Earth
  Optimum Coordinates
Test Results
  .PNG screen shot artifacts
  .log for MD5
  results text file contains logs of tests and status
  *Db.csv contains screen data gathered during collection

## Slide 18: Command and Control Collected Status Database Export
Export Screen Status data collected during and NLG Poll from database to a csv file
Database Table
  Select NMSPM Status or Terminal Status
  Select data collection window to export by specifying start and stop times (in GMT)
  Click Export button, and then click Test Results link to see the file
    Naming convention is <tblname>_<start as YYYYMMDDHHMMSS>_<stop YYYYMMDDHHMMSS>
    (Enhance to use popup)
  The columns of the file are group id, poll time, and n-columns named after each field on the captured screen(s), e.g.
    FL_EsNo is EsNo reported on the Forward Link section of the General Status Page, and
    FLS_EsNo is EsNo reported on the Terminal Forward Link Status page

## Slide 19: Command and Control Utilities
Map Bundles Test Report
  Post processes results from specified group(s) to text file containing gleaned information needed to prepare QA test report
    Select groups, checkboxes
    Click on Create
    Click Test Report to read report, or right-click “save link as” to upload report

## Slide 20: Command and Control ReDa
Summary Dashboard
  Current Station Status
    Indicates which Terminals are in use and which are free
  Summary Test Results
    Recent Test Queries
    Results Icon
      Click to load zip file of all results from group into browser download

## Slide 21: Use Cases - Map
mapBun Trickle
NMS
  Copy bundle
  trickle to download the bundles
Terminal CLI
  Get md5 checksum
Verification
  successful file transfer to Terminal by version number on Terminal GUI
  md5 checksum matches Terminal upload MD5
Run for signed and unsigned
mapBun Terminal Upload
Terminal GUI
  Load maps through GUI
Terminal CLI
  Get md5 checksum
Verification
  successful file transfer to Terminal by version number on Terminal GUI
  md5 checksum matches Trickle MD5
Run for signed and unsigned

## Slide 22: Use Cases - Map
mapBun Precedence
Test Controller
  Generates kml file
  Finds all coordinates
    Automatically generated
    Optimized to use single, unique coordinate for overlapping regions
      In diagram below, Lat/Long “P2” verifies satellite beam S1 and S2
Verification
  Search order of mapbunPrecVerify.log matches coords_precname.csv
mapBun FL Lock
NMS
  Set FL frequency based on map coordinates
    EMS Configuration
      Set Frequency, Chip Rate
  Compute FL frequency
    Formula:
Terminal
  Load SED/SSCF file bundles
    Optimize if loaded from previous portion of test
  Change the lat/long coordinates of the terminal and turn sat search on.
  Clear syslogMsgs file
  Reboot the system
  grep the syslogMsgs file
  Save satellites locked onto
Verification
  Examines satellite locking order for correctness

## Slide 23: Use Cases – NLG Collection
Poll Start
Polls NMSPM VMT associated to the group
  Polls approximately every 60 seconds and saves screen info to NMSPM Status database (inside Automation tool) that can be exported to CSV
  Accesses NMSPM through “Map” of the configured NMS
  Selects VMT based on the Configured Terminal Name
Polls Terminal associated to the group
  Polls approximately every 45 seconds and saves screen info to Terminal Status database (inside Automation tool) that can be exported to CSV
  Selects VMT based on the Configured Terminal Name
Select multiple groups to poll different terminals simultaneously
Poll Term-only Start
Polls Terminal associated to the group
  Polls approximately every 45 seconds and saves screen info to Terminal Status database (inside Automation tool) that can be exported to CSV
  Selects VMT based on the Configured Terminal Name

## Slide 24: Use Cases – NLG Collection
Poll Stop
Stops the active polling for the group(s)
  Works for Poll Start or Poll Term-only Start
Waits until next poll cycle
Captures Charts for NMSPM based on the duration between start and stop
Exports NMSPM Status and/or Terminal Status to to CSV based on duration
scp‘s syslogs from Terminal and RTNMS and post processes into .csv files for analysis
VMT Commands
Issues Logout, Relogin, Reboot to all groups specified in Group Id
  If only 1 group, just as easy to do directly
  Issued on the configured NMS
  Selects Hub associated RTNMS configuration
Currently does not support Beam Redirect

## Slide 25: VMT Commands
Issues NMS VMT Command(s) across 1 or more Group(s) (serially)
  Logout
  ReLogin
  Reboot
  Beam Re-Direct (Not Implemented)

## Slide 26: Map Testing Process
Steps
Pre-Release Meeting
  System Engineering walk-thru on upcoming map features
eMail
  Describes bundles for test and Perforce location
Perforce
  Get bundles to local workspace
  Review changes specified in RDD
SGT Tool
Pre Test Planning
  Determine Beams
Configuration
  Set up beams and maps according to plan
Automation
  Tests and Generates Results
Data Analysis
  Scripts (alResults.sh)
Reporting
  Analysis, PPT, KML
  Perforce
Automation Test Cases
SGT Tool
Upload
Trickle
Precedence
FL
  AL1 Normal
  AL2 Pilots
  Spectral Inversion

## Slide 27: Map Bundle Training Exercise
Map at //Arclight/ArcLight/Releases/oldreleases/SED_SSCF_Releases/Agile_Documents/Bundles_v1.184/
Test Unsigned only
Satellite Beam: SES-4(26.55/K/A/N)
Prepare a new test report (Datasheet only)
Hints:
  Automation Browser at 192.168.136.92, Connect Cisco VPN first
  All physical connection are correct to run this test
  Use Group 498 as an example
  Create Group 505 (CAREFULLY load 498, and CHANGE Group Id to 505 and then set parameters and save – separate save button for each section)
  Terminal 5 (is currently using SW ver 5.2.0.27) pw hint bob, **** use \’ to enter an apostrophe ‘
  Unsigned does not have the “vca00…sgn” in filename
  Look at results file to see test progress
  Run 1 test at a time
  Version is in the Perforce path
  Datasheet Example at //Arclight/ArcLight/SystemTest/TestReport/SED_SSCF/Bundles_v1.183_v1.184/Datasheet_v1.183_v1.184.xlsx

## Slide 28: NLG Data Analysis
Status CSV file(s)
  Screen values captured on regular time intervals
  Import into EXCEL
  Plot column(s) to see changes during test
  Example RL Data Rate
    Correlate NMS charts to data reported.
    Validates display at Term matches data at NMSPM
Syslog CSV file(s)
  Generated by post-processor
  Syslog reorganized into Specific Event columns of binary event triggers (0/1)
  Plot several columns over same time period and offset to see “triggers” over time
    NOTE: CRL login Bug revealed (2 or 3 peaks instead of 1)

## Slide 29: Post-Processed Syslog CSV File Formats
Terminal Syslog CSV
Currently, the following events are parsed, i.e. columns:
  POLLSEC, POLLTIME, VARG_1, VARG_2, SAT_SRCH, SAT_LOCK, BRL_LOGIN, CRL_LOGIN, LOGOUT_CMD, REBOOT_CMD, RELOGIN_CMD, TOD_RESET, SET_ANT, DWELL_TIMEO, SAT_HANDO, RLC_STATE, SMS_STATE, BB_STATE, LOGIN_STATE, TERM_STATE, UPD_ANTTXB, SEND_ANTSAT, MODE_CHG
Each event is represented with a "1" in the event column, and any supporting info is in the VARG column(s) as follows:
  If TOD_RESET, then VARG_1 is TOD_NEW and VARG_2 is TOD_OLD
  If SET_ANT, then VARG_1 is BEAM_NAME and VARG_2 is 0
  If *_STATE, then VARG_1 is state change value and VARG_2 is 0
  If SEND_ANTSAT, then VARG_1 is AcuSt and VARG_2 is 0
  If UPD_ANTTXB, then VARG_1 is AcuSt and VARG_2 is 0
RTNMS Syslog CSV
Currently, the following events are parsed, i.e. columns:
  POLLSEC,POLLTIME,VARG_1,VARG_2,VMT_STATE,CRL_STATE,CONN_LOGIN,CONN_OPER,CONN_SESS,PWRCTL_UPD,ACSM_UPD,CONN_LOGOUT,CONN_Vmt,CONN_VMT,CONN_RL
Each event is represented with a "1" in the event column, and any supporting info is in the VARG column(s) as follows:
  VARG_1 is Terminal ID (decimal equiv of 0.0.c.d addr), or CRL indicator for CRL_STATE
  VARG_2 is State for VMT_STATE or CRL_STATE, otherwise contains message

## Slide 30: Extra Slides & Master Diagrams

## Slide 31
AL AUTOMATION
GUI
(HTTP)
Linux
(SSH)
Unit Under Test (UUT)
NMS/EMS/ HUB
Term
Automation SW
Browser
DB
Test Automation
Subsystem
Test Equipment
Unit Under Test (UUT)
Browser

## Slide 32
S4 Catalyst
NetInstall-open SuSE
192.168.136.41
(u:root/p:viasat)
Map Test Appliance – Supermicro Blade #2
EMS
(VM-SuSE)
192.168.136.82
192.168.136.92 192.168.142.5 (VLAN-142)
192.168.136.142 192.168.142.8 (VLAN-142)
192.168.142.18 (VLAN-142)
<testerA>-wxp
<testerB>-wxp
Perforce, Share-point, …
Corp
LAN
Automation (VM-CentOS)
IPE
(VM-SuSeE)
RtNMS
(VM-SuSE)
NMS
(VM-SuSe)
Notes:
Cisco VPN Client AT_NOC_VPN
Connect VMBR-Rx to EFLM as needed
SAM4/FLM4 for 3LL Pilot
Mixer for Spectral Inversion
EFLM
Terminal
IF-SMA-RG6
EFLM-Tx
VMBR-Rx
192.168.142.58
(VLAN-142)
(VLAN-803-82x)
SIG GEN
VSwitch
<testerC>-wxp
Lab Switch/PBR
192.168.136.6-#2 (E2442)
136.6-#8 (E2448)
MIXER
“Base-ball Switch”
L
R
I
SAM4/FLM4

## Slide 33
S1:
P1
S2:
P2 P3
= {P2}